## Slide 1: Individual homework
Iancu Gheorghe-Aurelian, group 913

## Slide 2
Exercise 4.3 Boolean functions
Simplify the following Boolean functions of 4 variables using Veitch diagrams:

## Slide 3
Theoretical results
Simplification of boolean functions
Informally, to simply a Boolean function given in disjunctive canonical form, means to cover all its minterms with a minimum number of maximul monoms and with a minimum number of overlaps.
The simplification process is formalized by the steps below:
The initial function f is transformed into DCF(f).
Factorization process => the set of maximal monoms M(f).
From the set of maximal monoms the central monoms are selected => C(f).
The case of the simplification algorithm is identified and all simplified forms are obtained.

## Slide 4
Simplification algorithm

## Slide 5
Theoretical results
Veitch-Karnaugh Diagrams Method
The cells in a Veitch diagram are arranged so that there is only a single variable change.
Adjancy(graphical neighborhood) relation is defined by a single variable change.
The diagrams are circular, meaning that the first row/column and the last row/column are neighbors.
Two minterms belonging to two neighbor cells factorize => simple factorization.
The result of k-factorization is a monom which contains the column variables of all 2k neighbor minterms.
The maximal monoms are obtained from the diagram by applying factorization as follows: for a Boolean function of n variables we try first: n-factorization, we continue with n-1 factorization, …,
simple factorization and 0-factorization(isolated minterms).

## Slide 6
Veitch-Karnaugh Diagrams Method
Factorization process => the set of maximal monoms M(f).
From the set of maximal monoms the central monoms are seleted => C(f).
The central monoms are the maximal monoms which cannot be coverred by the disjunction of all the other maximal monoms.
Identification of the central monoms:
  If the group of the minterms coverred by a maximal monom contains at least one cell circled once, then the maximul monom is a central and it belongs to all the simplified forms of the function.
The groups of the minterms corresponding to the central monoms are shaded in the diagram.
The minterms from the function's expression which are unshaded, are not coverred by the central monoms and they will be coverred in all the possible ways using a minimum number of unused maximal monoms and with a minimum number of overlaps, resulting all the simplified forms of the initial function.

## Slide 7
Problem solution
Step 1: Obtain the Disjunctive Canonical Form (DCF):
DCF = function written as a disjunction of minterms corresponding to the 1 values of the function
We do so by breaking down each monom into all the minterms that are smaller than it.
(x1, x2,x3,x4) = x1x2 ∨ x1x̄2x̄3x̄4 ∨ x̄1x̄2x̄4 ∨ x̄1x̄3∨ x3x4 =
= x1x2x3x4 ∨ x1x̄2x̄3x4 ∨ x1x̄2 x3x4 ∨ x1x2x̄3x4 ∨ x1x̄2x̄3x̄4 ∨ x̄1x̄2x3x̄4 ∨
x̄1x̄2x̄3x̄4 ∨ x̄1x2x̄3x4∨ x̄1x̄2x̄3x4 ∨ x̄1x2x̄3x̄4 ∨ x̄1x̄2x3x4 ∨ x̄1x2x3x4=
= m15 ∨ m9 ∨ m11 ∨ m13 ∨ m8 ∨ m2 ∨ m0 ∨ m5 ∨ m1 ∨ m4 ∨ m3 ∨ m7

## Slide 8
Step 2: Find the maximal monoms:
We represent all the minterms we obtained in the Veitch diagram.
We then try to obtain the maximal monoms
m15 | m13 | m5 | m7
 |  | m4 | 
 | m8 | m0 | m2
m11 | m9 | m1 | m3
x2
x̄2
x1
x̄1
x̄3
x3
x3
x4
x4
x̄4

## Slide 9
m15 | m13 | m5 | m7
 |  | m4 | 
 | m8 | m0 | m2
m11 | m9 | m1 | m3
Triple factorization:
max1 = m15 ∨ m13 ∨ m5 ∨ m7 ∨ m11 ∨ m9 ∨ m1 ∨ m3 = x4
Double factorization:
max2 = m5 ∨ m4 ∨ m0 ∨ m1 = x̄1x̄3
max3 = m0∨ m2 ∨ m1 ∨ m3 = x̄1x̄2
max4 = m8 ∨ m0 ∨ m9 ∨ m11 = x̄2x̄3
We do not have simple factorization because
the others already cotain them.
Therefore, M(f) = {max1, max2, max3, max4}

## Slide 10
Step 3: Find the central monoms:
A central monom is a central monom that contains at least one minterm that is not part of any other maximal monom.
In our case max1(because no other maximal monom contains m15), max2(because no other maximal monom contains m4), max3(because no other maximal monom contains m2) and max4(because no other maximal monom contains m8)
C(f) = {max1, max2, max3, max4}

## Slide 11
Step 4: Identify the case of the simplification algorithm and write the simplified form(s)
Since C(f) == M(f) => first case -> we have a unique simplification
fs(x1,x2,x3,x4) = max1 v max2 v max3 v max4 = x4 v x̄1x̄3 v x̄1x̄2v x̄2x̄3
m15 | m13 | m5 | m7
 |  | m4 | 
 | m8 | m0 | m2
m11 | m9 | m1 | m3